AWC608

1．POW  Power interface

| Pin | Definition |
| --- | --- |
| 1 | +24V, Positive power supply |
| 2 | GND, Negative power |

- OUT   Out interface

| Pin | Definition |
| --- | --- |
| 1 | DC24V, Power(OUT) |
| 2 | OUT1, Blowing signal(The whole process of blowing) The machine is idle, the motherboard output OUT1 high； The machine is working, the motherboard output OUT1 is low。 |
| 3 | OUT2, Blowing signal(The whole process of blowing) The machine is idle, the motherboard output OUT1 high； The machine is working, the motherboard output OUT1 is low |
| 4 | GND, Power ground(OUT) |

3.OUT Out interface

| Pin | Definition |
| --- | --- |
| 1 | DC24V, Power(OUT) |
| 2 | OUT3, Output signal (reservations) |
| 3 | OUT4, Output signal (reservations) |
| 4 | GND, Power ground(OUT) |

4.Laser2   Laser 2 interface

| Pin | Definition |
| --- | --- |
| 1 | DC5V, Power(OUT) |
| 2 | PROTECT, Water protection input signal |
| 3 | PWM, Laser power |
| 4 | TTL, Laser switch signal |
| 5 | GND, Power ground(OUT) |

5.Laser1  Laser 1 interface  Similar  the 4 .laser2

The laser interfaces with the the universal laser power connection as shown below

6.X/Y/Z/U axis interface

| Pin | Definition |
| --- | --- |
| 1 | DC5V, Power(OUT) |
| 2 | PUL, Pulse signal |
| 3 | DIR, Direction signals |

The interface with the drive connected as shown below:

7.X / Y limit interface

| Pin | Definition |
| --- | --- |
| 1 | DC24V, Power(OUT) |
| 2 | ELY+; the upper limit of Y_axis the axis movement to the sensor signal input signal at the maximum coordinate limit |
| 3 | ELX+; the upper limit of X_axis the axis movement to the sensor signal input signal at the maximum coordinate limit |
| 4 | ELY-; The lower limit of the Y-axis, the axis movement to a minimum at the coordinate (zero position) limit sensor signal input signal. |
| 5 | ELX-; The lower limit of the X-axis, the axis movement to a minimum at the coordinate (zero position) limit sensor signal input signal.。 |
| 6 | GND Power ground(OUT) |

8.Z/U limit interface

| Pin | Definition |
| --- | --- |
| 1 | DC24V, Power(OUT) |
| 2 | ELU+; the upper limit of U_axis the axis movement to the sensor signal input signal at the maximum coordinate limit |
| 3 | ELZ+ the upper limit of Z_is the axis movement to the sensor signal input signal at the maximum coordinate limit |
| 4 | ELU-; The lower limit of the U-axis, the axis movement to a minimum at the coordinate (zero position) limit sensor signal input signal. |
| 5 | ELZ- The lower limit of the Z-axis,the axis movement to a minimum at the coordinate (zero position) limit sensor signal input signal.。 |
| 6 | GND Power ground(OUT) |

8.IN  put interface

| Pin | Definition |
| --- | --- |
| 1 | DC24V, Power(OUT) |
| 2 | IN1, Cap protection signal (input), active low |
| 3 | IN2, The footswitch signal (input), active low |
| 4 | GND Power ground(OUT) |

9.IN  input interface

| Pin | Definition |
| --- | --- |
| 1 | DC24V, Power(OUT) |
| 2 | IN3, Input signal (reserved) |
| 3 | 1N4, Input signal (reserved) |
| 4 | GND Power ground(OUT) |

10.IN  input interface

| Pin | Definition |
| --- | --- |
| 1 | DC24V, Power(OUT) |
| 2 | IN3, Input signal (reserved) |
| 3 | 1N4, Input signal (reserved) |
| 4 | GND Power ground(OUT) |